Pa0nhc PCB catalog.
Ver : 2024.10.09 Copyright pa0nhc.
World wide free shipment (except otherwise mentioned).
You get an Email when I posted your goods.
Track and trace + insurance costs upto 35 Euro's extra !
All technical info and building instructions are available on : www.pa0nhc.nl

---
Pure Signal power tap for Hermes Lite2.
50 Ohms output : -1dBm peak.
Adjustable for 100W or 400W or 1600W peak input.
12Vdc PTT.
Fits into a Hammond 1590C ALU box.
www.pa0nhc.nl

---
20210825
“Double Delta Loop” ©.
Unique small 145MHz omni directional
horizontal polarized
low power loop antenna.
Building kit contains:
Loop PCB 162 x 195 mm.
1 ferrite core.
1 meter lacqured 0.25 mm wire.
2 capacitors.
1 hairpin match wire.
See setup details at www.pa0nhc.nl
Price : 30 Euro.

---
Transformer PCB for pure magnetic, permanent outdoor, transmit + receive loop antenna.
Balanced, 3-band, high efficiency. © 20200617.
Professional double sided matching PCB : 27.50 Euro
New 210x80mm design with smaller but improved CMC.
Bigger connection strips and more space for different types of
40m and 80m series tune capacitors.
Usable capacitors : Mica, MKP2, polyester low inductance.
Also usable for a mono band loop.
Read full development, construction and adjustment details on www.pa0nhc.nl

---
Pa0nhc version of an active receiving loop antenna. 20201020.
2 PCB set : 25 Euro

---
ON9BOG / PA0NHC
50 ohm 0dBm generator
for calibration of
S-meters.
Complete 7 PCB set
including housing.
20.- Euro

---
Fixed 50 ohm 63dB attenuator
for calibration of
S-meters.
Output :
(with 0dBm generator)
S9+10dB.
Complete 7 PCB set
including housing.
20.- Euro

---
1 dB step attenuator
50 ohm 73dB max.
for calibration of
S-meters.
Good quality cheap tumbler switches.
Circuit PCB : 16.- Euro
Output with 0dBm generator is
S9+73dB to S9.
Output with 0dBm generator
and
63dB attenuator is
S9+10dB tot S9-63dB..

---
Main unit PCB:
20.-- Euro
(NO antenna unit PCB available !)
“Xfilt”
pa0nhc
active
RF noise
canceller
Prototype.

---
Automatic loop tuner.
Updated PCB designs : component locations, component Ids, less wiring.
PCB set : 27.50 Euro. A4 manual : 12.50 Euro.

---
Unique pa0nhc
small active, very selective
magnetic (H-field)
NVIS receiving antenna.
If installed rotateable,
vast suppression of local noises
is possible
Build-in noiseless power supply.
PCB set : 30.-- Euro.

---
Pa0nhc version of the MINIWHIP.
Active wideband receiving antenna.
10 kHz tot > 30 MHz. IP3 : 30 dBm.
PCB sets are SOLD OUT.
If available agian, it will be published here.
READ FIRST on my site :
“The accordances and differences between E-field and H-field antennas”

---
AM modulated (3,58 MHz) mini TX 65 mW.
Build-in tuner for whip or short wire antenna, ground / counterpoise.
AM modulation : 3 tones x 3 tempi = 9 different modulations.
6-9 Vdc / 40 mA, at least 5 uur stable operation on 9V battery.
PCB : 16.-- Euro.
10 pieces : ask price.

---
Optimal analogue 145 MHz ARDF receiver.
Very sensitive, very selective, large sensitivity range adjustment.
New version PCB : 20.-- with larger holes and new coil connections for easy use of different still available coils and coil sets. Mean current consumption only 9V / 15 mA.
Tune range abt. 1MHz. Only suitable for experienced builders. Want 10 pieces ? Ask price.

---
Optimal analogue 3.5 MHz ARDF receiver.
Fully balanced input circuits : antenna, buffer, mixer.
New version PCB including new coil connections for easy use of different still available coils. 9V / 30 mA. Tune range abt. 100KHz (3.5 to 3.6 MHz).
PCB : 20.--. 10 pieces ? Ask price.

---
50 ohm directional stripline couplers.
29 to 435 MHz. 3x DC output / 3x HF output.
See next page for available types.
Coupling attenuation : abt. 31dB @ 145M MHz Through line impedance : 50 ohm.
RF output impedances : 50 ohm.. DC output resistance : 100 k. Directivity : typical 25 to 30dB @ 145 MHz.
RF output abt. 1Veff for input : 750W @ 29 MHz, 30W @ 145 MHz, 10W @ 435 MHz (6 dB / octave).
One PCB : 12.50 Euro. Every PCB more : 5 Euro extra.

---
DC371 DC372 DC coax
RF371 RF372 RF coax

---
Preamp 28 – 440 MHz.
Low noise, Hi-IP, sturdy. PCB : 12.50 Euro
Protototype

---
pa0nhc magnetic nearfield indicator.
Accurate differences in sampled nearfield strength.
? Is your loop only tuned for best VSWR,
or also for maximal magnetic field strength ?
Set of 2 PCB's : 16 Euro.

---
RF low power meter. Measures really RMS values.
Range : -35 dBm to +6 dBm.
Reasonably accurate from 32 kHz to 800 MHz (max. 2,8 GHz).
Internal 50 ohm load and overvoltage protection. Power : 4 to 5V battery, max. 8mA..
Immediately useable values without the need to calabrate
Set of two different versions PCB's : 16 Euro.

---
RF power meter. Measures really RMS values.
Range : 20 mW tot 200 W. 32 kHz tot 146 MHz (max. 2,8 GHz).
Through-line impedance : 50 ohms. External 50 ohm load. Overvoltage protection
Power : 4 to 5V battery max. 8mA..
Immediately useable values without the need to calabrate
PCB prijs : 16 Euro.